UC-1/10 and UC-3/20

PUMP WITH PUMPING EQUIPMENT

FOR EXCHANGER CHEMICAL CLEANING

TECHNICAL INFORMATION

|  | a) UC-1/10 | 2) UC-3/20 |
| --- | --- | --- |
| Installed power N | 0.37kW | 0.55kW |
| Tank volume V | 60dm3 |
| Material - polypropylene | PP-DWS |
| Size: | 700x900 | 800x518x845 |
| Total weight | 25 kg | 30 kg |
| Voltage U | ~220V |

PUMP with a single- or three phase motor

|  | UC-1/10 | UC-3/20 |
| --- | --- | --- |
| Capacity Q | 1m3/h | 3m3/h |
| Elevation head H | 10m | 20m |
| Material | polypropylene, acid resistant steel |

HEATER 	P = 1 x 1.5 kW

UC-1/10-1; UC-3/20-1 with a heater

The PUMP WITH PUMPING EQUIPMENT is designed for chemical cleaning of heating installation and equipment by removing boiler scale and corrosion products.

TYPES UC-1/10 and UC-1/10-1 are intended for cleaning low-flow exchangers and vertical pipelines up to 10 m.

TYPES UC-3/20 and UC-3/20-1 are intended for plate heat exchangers, heat exchanger packages and vertical pipelines up to 20 m.

The inbuilt distributor allows changing the direction of bath pumping without switching off the pump.

The pump set control box ensures safe equipment operation. The applied plastics, i.e. PP and PVDF, make it fully chemically resistant to such media as mineral acids, nitric acid, phosphoric acid and organic acids, such as formic, acetic, citric acid and soda lye.