UC-10/40-1-M and UC-10/40-1-M EXTENDED

PUMPS WITH PUMPING EQUIPMENT

FOR EXCHANGER CHEMICAL CLEANING

The UC 10/20-1-M and UC 10/40-1-M PUMPS WITH PUMPING EQUIPMENT are designed for chemical cleaning of great volume heating installation and equipment by removing boiler scale and corrosion products.

Inbuilt heaters allow work in higher temperature 40o÷60oC.

The inbuilt distributor allows changing the direction of bath pumping without switching off the pump.

The control box of UC 10/20-1-M and UC-10/40-1-M pump set ensures safe equipment operation. The applied plastics, i.e. PP and PVDF, make it fully chemically resistant to such media as mineral acids, nitric acid, phosphoric acid and hydrochloric acid as well as organic acids, such as formic, acetic, citric acid and soda lye. The UC 10/20-1-M and UC-10/40-1-M equipment can also be used as a mixer, intermediate pumping station or a reactor.

TECHNICAL INFORMATION

|  | UC-10/20-1 | UC-10/40-1 | -M |
| --- | --- | --- | --- |
| Installed power N | 4.5 kW | 5.5 kW | 6 kW |
| Tank volume V | 150 dm3 | 300 dm3 |
| Material - polypropylene | B-200 – DWST |
| Size | 660x700x1100mm | 860x820x700 |
| Total weight | 35 kg | 25 kg |
| Voltage U | ~220V | ~220V380V | ~380V |

PUMP

|  | UC-10/20-1 | UC-10/40-1 |
| --- | --- | --- |
| Capacity Q | 10m3/h | 10m3/h |
| Elevation head H | 25m | 40m |
| Material | polypropylene, acid resistant steel |

HEATERS

Heater efficiency 	P = 2x1.5kW