ZP 160-15 Pump Set

Mobile pump set designed for pumping Biorenex – Bioruster series preparations and Neutraliser.

The pump, including motor and switching collector, is installed on a platform with a frame made of stainless tubes.

The pump set consists of:

- pump with motor type 3MHS-65-160/15

- Ø 65 collector switching flow directions equipped with ball valves, a non-return valve and a cut-off valve

- platform with a frame made of stainless tubes, the platform is equipped with a stainless plate and ground wheels with brakes.

- electrical installation, including control and protection /in a box/

Pump with motor type 3MHS-65-160/15 – technical data:

- power 15 kW

- supply voltage 400 V

- max. electricity consumption 30 A

- max. efficiency  Q -138 m³/h

- max. elevation head H- 45 m

- revolutions per minute – 2900 r.p.m.

- weight 93 kg

- the pump itself is made of ASI 304 steel

- size ( length x width x height )  732 x 296 x 360 mm

- suction manifold Ø 80 mm (flange Ø 200 )

- force main Ø 65  (flange Ø 185 )

- VITON-type resistant to chemicals shaft seal